Form 3 (3)

Name of proposer:

Title of proposed subject:

[Basic conditions]

| Details of the proposal | Allocation of marks (Basic points) |
| --- | --- |
| (1) Decontamination performance The decontamination speed of tank is presented. Decontamination factor (DF as the ratio of dose rate before and after decontamination) is assumed at target decontamination performance for the tank whose maximum dose rate before decontamination is 10 mSv/h as 70 micro-meter dose equivalent of beta ray measured at 5 mm from the surface of tanks is presented. Devices with which the decontamination effect can be evaluated simultaneously in decontamination works are presented. | 5 |
| (2) Concepts for waste Suggestions to reduce the amount of liquid waste as low as possible are presented. Concepts for reduction or recover secondary wastes are presented. | 5 |
| (3) Countermeasure for curved inner surface of tank and joints Technologies to enable the decontamination of curved inner surface of tank and joints are presented. | 5 |
| (4) Countermeasure for tanks located in the area of tank yards Technologies to decontaminate tanks located in the area of tank yards. | 5 |

[Additional Point Items]

| Details of the proposal | Allocation of marks (Technical points) |
| --- | --- |
| (1) Decontamination performance Decontamination performance is high. The decontamination speed is high for proposed decontamination performance The number of workers for decontamination is small. The required space for decontamination works and exchanging the equipment is small. | 26 (7) (7) (5) (7) |
| (2) Suppression of waste generation The amounts (mass and volume) of generated wastes are small. The wastes can be recovered or no problem will occur without recovery. | 8 (4) (4) |
| (4) Presentation of experimental data The experiment is conducted and the data are analyzed from various points of view to confirm the effect. Based on the presented data, it is expected to be shorten the time period for demonstration. | 6 (2) (4) |

The evaluations for technical points are classified into four classes; A (factor is 5/5), B (3/5), C (1/5), D (0/5), and the technical points will be calculated by multiplying the allocated points with the factors of each class.