Form 4

[Basic requirements]

| Details of the proposal | Allocation of marks (Basic points) |
| --- | --- |
| i) Tritium separation performance and its mechanism The technology which can achieve a separation factor more than 100 of the tritiated water arising in the Fukushima Daiichi Nuclear Power Station is described. The separation mechanism is described in detail. Generation volume, composition and storage method of tritium concentration liquid containing enriched tritium and effluent (if generated) are described in detail. The volume of needed “treated water” for implementing the demonstration tests is described. (The contents of the “simulated water” are described if the applicant plans to use it.) | 5 |
| ii) Treatment capacity It is described that the treatment capacity of the technology can be expanded to more than 400 m3 per day. Possible verification steps are described in detail. Both the treatment capacity in the verification tests and the one which can be achieved in the said expansion (unit: m3 per day) are described. The system for achieving the treatment capacity is described in detail. | 5 |
| iii) Construction costs and operating costs in expansion and construction time period Construction costs and operating costs, including the method of their estimations and the conditions, are described in detail. Construction time period, including the method of its estimation and the conditions, is described in detail | 5 |
| iv) Necessary site area and height of the system per treatment volume The necessary site area for treatment per 400m3 of “treated water”, including the method of its estimation and the conditions, is described in detail. The necessary height of the system is described in detail (using meter as the unit). | 5 |

[Points to be additionally added]

| Details of the proposal | Allocation of marks (Technical points) |
| --- | --- |
| i) Tritium separation performance The separation efficiency of the proposed technology is high. | 10 |
| ii) Effluent Generated effluent is small. | 3 |
| iii) Necessary site area per treatment volume The necessary site area for treatment of 400m3 of “treated water” per day is narrow. | 9 |
| iv) Time needed for treatment of 800,000 m3 of “treated water” Days needed for treatment of 800,000 m3 of “treated water” is short. | 3 |
| v) Presentation of the experimental data The experimental data are with control samples and with data statistically processed and evaluated. The data are already published as peer reviewed in an academic conference, journal, etc. The experiment is conducted and the data are analyzed from various points of view to confirm the effect. Based on the presented data, it is expected to shorten the time period for demonstration. | 11 （3） （3） （2） （3） |
| vi) Necessary scheme for expansion of the technology Whether or not expected time needed for development and demonstration is short, and the process is specific. Whether or not the scheme for consideration is sufficiently arranged. | 4 （2） （2） |

※For evaluation of the technical points, each item will be scored as A (factor of 5/5), B (3/5), C (1/5), or D (0/5). The technical points are calculated by multiplying the allocated points with the factors of each class.